## Slide 1: Lecture 15 – Networking Concepts
Michael Bailey
University of Illinois
ECE 422/CS 461 – Spring 2016

## Slide 2: Circuit and Packet Switching
Circuit switching
  Legacy phone network
  Single route through sequence of hardware devices established when two nodes start communication
  Data sent along route
  Route maintained until communication ends
Packet switching
  Internet
  Data split into packets
  Packets transported independently through network
  Each packet handled on a best efforts basis
  Packets may follow different routes

## Slide 3: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 4: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 5: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 6: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 7: Network Layers
Network models typically use a stack of layers
  Higher layers use the services of lower layers via encapsulation
  A layer can be implemented in hardware or software
  The bottom-most layer must be in hardware
A network device may implement several layers
A communication channel between two nodes is established for each layer
  Actual channel at the bottom layer
  Virtual channel at higher layers

## Slide 8: Reference Models
OSI Model
Application
Physical
Link
Network
Transport
Session
Presentation
Physical
Net. Interface
Internet
Transport
Application
1
2
5
4
3
6
7
Internet Model
Not Specified
ARP, RARP
IP (ICMP)
TCP, UDP
FTP, HTTP
Internet Protocol Suite

## Slide 9: Protocols
A protocol defines the rules for communication between computers
Protocols are broadly classified as connectionless and connection oriented
Connectionless protocol
  Sends data out as soon as there is enough data to be transmitted
  E.g., user datagram protocol (UDP)
Connection-oriented protocol
  Provides a reliable connection stream between two nodes
  Consists of set up, transmission, and tear down phases
  Creates virtual circuit-switched network
  E.g., transmission control protocol (TCP)

## Slide 10: Layering of protocols
SONET
TCP
IP
Ethernet
ATM
SSH
DNS
UDP
HTTP
NNTP
SMTP
FTP
Application layer
Network layer
Link layer
Transport layer

## Slide 11: Encapsulation
A packet typically consists of
  Control information for addressing the packet: header and footer
  Data: payload
A network protocol N1 can use the services of another network protocol N2
  A packet p1 of N1 is encapsulated into a packet p2 of N2
  The payload of p2 is p1
  The control information of p2 is derived from that of p1
Header
Payload
Footer
Header
Payload
Footer

## Slide 12: Internet Layers
Application
Transport
Network
Link
Application
Transport
Network
Link
Network
Link
Network
Link
Ethernet
Fiber Optics
Wi-Fi
Physical Layer

## Slide 13: Internet Packet Encapsulation
Application Packet
TCP Data
TCP
Header
IP
Header
Frame
Header
Frame
Footer
Link Layer
Network Layer
Transport Layer
IP Data
Frame Data
Application Layer

## Slide 14: Network Interfaces
Network interface: device connecting a computer to a network
  Ethernet card
  WiFi adapter
A computer may have multiple network interfaces
Packets transmitted between network interfaces
Most local area networks, (including Ethernet and WiFi) broadcast frames
In regular mode, each network interface gets the frames intended for it
Traffic sniffing can be accomplished by configuring the network interface to read all frames (promiscuous mode)

## Slide 15: MAC Addresses
Most network interfaces come with a predefined MAC address
A MAC address is a 48-bit number usually represented in hex
  E.g., 00-1A-92-D4-BF-86
The first three octets of any MAC address are IEEE-assigned Organizationally Unique Identifiers
  E.g., Cisco 00-1A-A1, D-Link 00-1B-11, ASUSTek 00-1A-92
The next three can be assigned by organizations as they please, with uniqueness being the only constraint
Organizations can utilize MAC addresses to identify computers on their network
MAC address can be reconfigured by network interface driver software
Notes: MAC addresses can be permanently burned in (BIA), or be a locally administered address (LAA) set by an administrator. A MAC address starting out with 00-08-74 for instance is assigned by Dell, while one starting out with 00-0a-95 is assigned by Apple. Despite the IEEE limitations on LAAs, most OSs allow you to specify an arbitrary MAC for an interface.

## Slide 16: Switch
A switch is a common network device
  Operates at the link layer
  Has multiple ports, each connected to a computer
Operation of a switch
  Learn the MAC address of each computer connected to it
  Forward frames only to the destination computer

## Slide 17: Combining Switches
Switches can be arranged into a tree
Each port learns the MAC addresses of the machines in the segment (subtree) connected to it
Fragments to unknown MAC addresses are broadcast
Frames to MAC addresses in the same segment as the sender are ignored

## Slide 18: Types of Wireless Networks
Infrastructure
  Client machines establish a radio connection to a special network device, called access point
  Access points connected to a wired network, which provides a gateway to the internet
  Most common type of wireless network
Peer-to-peer
  Multiple peer machines connect to each other
  Typically used in ad-hoc networks and internet connection sharing
Access Point
Client
Wired LAN
Client
Client
Peer
Peer
Peer
Peer

## Slide 19: Internet Protocol
Connectionless
  Each packet is transported independently from other packets
Unreliable
  Delivery on a best effort basis
  No acknowledgments
  Packets may be lost, reordered, corrupted, or duplicated
IP packets
  Encapsulate TCP and UDP packets
  Encapsulated into link-layer frames
Data link frame
IP packet
TCP or UDP packet

## Slide 20: IP packet layout
IP header includes
  Source address
  Destination address
  Packet length (up to 64KB)
  Time to live (up to 255)
  IP protocol version
  Fragmentation information
  Transport layer protocol information (e.g., TCP)

## Slide 21: IPv4 Packet Header Format
4-bit
version
4-bit
hdr len (bytes)
8-bit
Type of Service
(TOS)
16-bit total length (bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit header checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload (e.g., TCP/UDP packet, max size?)
20-byte
Header
usually IPv4
usually 20 bytes (without options)
IP fragmentation
error
check
header
max number
remaining hops
(decremented at
each router)
upper layer protocol
to deliver payload to,
e.g., ICMP (1), UDP (17), TCP (6)
e.g. timestamp,
record route
taken, specify
route

## Slide 22: IP Addressing
IP address used to route datagrams through network.
IPv4 32 bit address, IPv6 128 bit address.
Divided into two parts: network and host.
Network part: Used to route packets. (ZIP code)
Host part: Used to identify an individual host. (House number)
Usually represented in dotted decimal notation: 141.211.144.212
Each number represents 8 bits: 0-255.

## Slide 23: Decimal representation of Internet addresses
octet 1
octet 2
octet 3
Class A:
1 to 127
0 to 255
0 to 255
1 to 254
Class B:
128 to 191
Class C:
192 to 223
224 to 239
Class D (multicast):
Network ID
Network ID
Network ID
Host ID
Host ID
Host ID
Multicast address
0 to 255
0 to 255
1 to 254
0 to 255
0 to 255
0 to 255
0 to 255
0 to 255
0 to 255
Multicast address
0 to 255
0 to 255
1 to 254
240 to 255
Class E (reserved):
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
240.0.0.0 to
255.255.255.255
Range of addresses

## Slide 24: Classless Interdomain Routing (CIDR)
Allow division between network and host portion on any bit boundary.
  More efficient use of address space.
  Allows division/aggregation of sub-assignments.
Networks now identified by network address and the length of the network portion: 141.213.8.0/24
Hosts identified by address and network mask: 141.213.8.1, 255.255.255.0.
WHY? Rapid depletion of class B address space and poor utilization of the assigned address space

## Slide 25: IP subnets
CIDR prefix length | Subnet Mask | Number of hosts
/8 | 255.0.0.0 | 224
/9 | 255.128.0.0 | 223
/10 | 255.192.0.0 | 222
/24 | 255.255.255.0 | 28 = 256
/25 | 255.255.255.128 | 27 = 128
/26 | 255.255.255.192 | 26 = 64
/27 | 255.255.255.224 | 25 = 32
/28 | 255.255.255.240 | 24 = 16
/29 | 255.255.255.248 | 23 = 8
/30 | 255.255.255.252 | 22 = 4

## Slide 26: Special IP addresses
Prefix | Suffix | Type of Address | Purpose
all-0s | all-0s | this computer | used during bootstrap
network | all-0s | network | identifies a network
network | all-1s | directed broadcast | broadcast on a specified net
all-1s | all-1s | limited broadcast | broadcast on a local net
127 | any | loopback | testing

## Slide 27: IP Address Space and ICANN
Hosts on the internet must have unique IP addresses
Internet Corporation for Assigned Names and Numbers
  International nonprofit organization
  Incorporated in the US
  Allocates IP address space
  Manages top-level domains
Historical bias in favor of US corporations and nonprofit organizations
Examples
  003/8 May 94 General Electric
  009/8 Aug 92 IBM
  012/8 Jun 95 AT&T Bell Labs
  013/8 Sep 91 Xerox Corporation
  015/8 Jul 94 Hewlett-Packard
  017/8 Jul 92 Apple Computer
  018/8 Jan 94 MIT
  019/8 May 95 Ford Motor
  040/8 Jun 94 Eli Lily
  043/8 Jan 91 Japan Inet
  044/8 Jul 92 Amateur Radio Digital
  047/8 Jan 91 Bell-Northern Res.
  048/8 May 95 Prudential Securities
  054/8 Mar 92 Merck
  055/8 Apr 95 Boeing
  056/8 Jun 94 U.S. Postal Service

## Slide 28: How To Bootstrap an End Host?
What local DNS server to use?
What IP address the host should use?
How to send packets to remote destinations?
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/24
5.6.7.0/24
1.2.3.7
1.2.3.156
???
1.2.3.19
router

## Slide 29: Avoiding Manual Configuration
Dynamic Host Configuration Protocol (DHCP)
  End host learns how to send packets
  Learn IP address, DNS servers, and gateway
Address Resolution Protocol (ARP)
  Others learn how to send packets to the end host
  Learn mapping between IP & interface addresses
host
host
DNS
...
host
host
DNS
...
router
router
1.2.3.0/24
5.6.7.0/24
1.2.3.7
1.2.3.156
???
1.2.3.19
router

## Slide 30
Problem: IP Address Exhaustion
IPv4 Addresses are 32 bits wide: ~3.7Bn usable addresses
All devices on the Internet require an address
Given Internet growth rate, addresses have been diminishing fast…
IANA exhausted free address pool in February 2011
1988: Started with 3.7Bn usable free;
By 1997: just 1.8Bn left

## Slide 31: Solution Strategies
Under address scarcity, how do we continue to support Internet growth?
Three ways of mitigating exhaustion of a scarce resource:
  Sharing:
    Share addresses in time via Dynamic Host Configuration Protocol (DHCP)
    Share addresses in port space via, e.g. Carrier-grade NAT (CGN)
  More efficient utilization:
    Stricter policy for new address allocations
    Reallocation of unused or otherwise reclaimed addresses
    Address markets for the efficient distribution of addresses
  Transition to another resource:
    Replace IPv4 with IPv6, which provides the ultimate long-term solution with a practically inexhaustible address space
Notes: This is the space of possible solutions... working on address scarcity and will talk about two of the solutions
Why study efficient util if will transition off v4?
IPv4 will last a long time, we will have coexistence, for availability and security of the Internet...
Why study v6 adoption?:
The Internet has never experienced a change so fundamental and large scale. From a Science perspective, studying this event is unique opportunity.

## Slide 32: Network Address Translation
Introduced in the early 90s to alleviate IPv4 address space congestion
Relies on translating addresses in an internal network, to an external address that is used for communication to and from the outside world
NAT is usually implemented by placing a router in between the internal private network and the public network.
Saves IP address space since not every terminal needs a globally unique IP address, only an organizationally unique one
While NAT should really be transparent to all high level services, this is sadly not true because a lot of high level communication uses things on IP
Notes: Whenever the router encounters a datagram it translates the address depending on what way the packet is headed
Usually any given internal IP address is bound to one of many IP addresses dynamically when it creates a session
NAT often needs to handle certain protocols like FTP in a special manner
While most NAT routers can handle popular protocols well, even when they need special attention, well, there are protocols which these routers cannot handle, and hence not all applications can run transparently through NAT.

## Slide 33: Translation
Router has a pool of private addresses 192.168.10.0/24
NAT route
global realm
private realm
192.168.10.237
s=192.168.10.237 d=128.148.36. 11
s=128.148.36.179
d=128.148.36.11
s=128.148.36.11
d=128.148.36.179
s=128.148.36.11
d=192.168.10.237
128.148.36.11

## Slide 34: A typical NAT-based home network (CDK Figure 3.18)

## Slide 35: IP Packet Modifications
source IP address
type of service
total length
ident
header checksum
destination IP address
options
data
vers
len
flags
fragment offset
time to live
proto
padding
0
31
Modified on input
Modified on output
????
Computed

## Slide 36: What is the Internet?

## Slide 37: What’s the Internet: “nuts and bolts” view
millions of connected computing devices: hosts, end-systems
  PCs workstations, servers
  PDAs phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 38: What’s the Internet: “nuts and bolts” view
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 39: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  Web, email, games, e-commerce, database., voting, file (MP3) sharing
communication services provided to apps:
  connectionless
  connection-oriented

## Slide 40: Internet design
Put the intelligence in the end hosts and keep the network simple.
  Packet switched instead of circuit switched.
  Best effort delivery.
  Force transport layer to deal with delay and loss.
Reliable in the face of failures.
  No session state on routers.
  Allows routers to be added and removed without causing large disturbances.

## Slide 41: Autonomous Systems (AS)
The Internet is a collection of autonomous systems.
AS: A set of routers and networks under the same administrative control.
Inter-domain vs. intra-domain routing.
R1
R5
R4
R2
R6
R3

## Slide 42: The Internet Backbone
http://advice.cio.com/node/209

## Slide 43: Internet structure: network of networks
roughly hierarchical
at center: “tier-1” ISPs (e.g., UUNet, BBN/Genuity, Sprint, AT&T), national/international coverage
  treat each other as equals
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-1 providers interconnect (peer) privately
NAP
Tier-1 providers also interconnect at public network access points (NAPs)

## Slide 44
Qwest’s backbone

## Slide 45: Internet structure: network of networks
“Tier-2” ISPs: smaller (often regional) ISPs
  Connect to one or more tier-1 ISPs, possibly other tier-2 ISPs
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP pays tier-1 ISP for connectivity to rest of Internet
tier-2 ISP is customer of
tier-1 provider
Tier-2 ISPs also peer privately with each other, interconnect at NAP

## Slide 47: Internet structure: network of networks
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
NAP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet

## Slide 48: UMnet Backbone

## Slide 49: Connection-oriented service
Goal: data transfer between end systems
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
Byte-steam abstraction: reliably delivering a stream of bytes from S to R
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 50: Network edge: connectionless service
Goal: data transfer between end systems
  Goal is same as before!
  No handshaking
  No connection state maintained on end hosts
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control
Apps using TCP:
HTTP (Web), FTP (file transfer), Telnet (remote login), SMTP (email)
Apps using UDP:
streaming media, teleconferencing, DNS, Internet telephony

## Slide 51: IP Routing
A router bridges two or more networks
  Operates at the network layer
  Maintains tables to forward packets to the appropriate network
  Forwarding decisions based solely on the destination address
Routing table
  Maps ranges of addresses to LANs or other gateway routers

## Slide 52: Interplay between routing and forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 53: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate the reachability information to all routers internal to the AS.
  Determine “good” routes to subnets based on reachability information and policy.
Allows a subnet to advertise its existence to rest of the Internet: “I am here”

## Slide 54: BGP basics
Pairs of routers (BGP peers) exchange routing info over semi-permanent TCP connections: BGP sessions
Note that BGP sessions do not correspond to physical links.
When AS2 advertises a prefix to AS1, AS2 is promising it will forward any datagrams destined to that prefix towards the prefix.
  AS2 can aggregate prefixes in its advertisement
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
eBGP session
iBGP session

## Slide 55: DNS: Domain Name System
People: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., www.eecs.umich.edu - used by humans
Q: map between IP addresses and name ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol host, routers, name servers to communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 56: DNS name servers
no server has all name-to-IP address mappings
local name servers:
  each ISP, company has local (default) name server
  host DNS query first goes to local name server
authoritative name server:
  for a host: stores that host’s IP address, name
  can perform name/address translation for that host’s name
Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
Maintenance
doesn’t scale!

## Slide 57: DNS Hierarchical Name Space
.com
.edu
.org
.ac
.uk
.zw
.arpa
unnamed root
bar
west
east
foo
my
ac
cam
usr
in-
addr
12
34
56
generic domains
country domains
my.east.bar.edu
usr.cam.ac.uk
12.34.56.0/24
.
Top-Level Domain (TLD)

## Slide 58: Distributed Hierarchical Database (1st Approx)
Root name servers
.com name servers
.org name servers
.edu name servers
poly.edu
name servers
umass.edu
name servers
yahoo.com
name servers
amazon.com
name servers
pbs.org
name servers
Client wants IP for www.amazon.com:
Client queries a root server to find .com name server
Client queries .com name server to get amazon.com name server
Client queries amazon.com name server to get IP address for www.amazon.com

## Slide 59: Name Space Distribution
124537172 arin.net
217003127 verisign.com
314529802 apnic.net
414526895 gslb.com
510917319 manitu.net
69167881 sorbs.net
78701029 msft.net
88595104 google.com
97520954 amazon.com
107450839 register.com
117034622 gtld-servers.net
126937887 facebook.com
136779616 coremetrics.com
146574735 msecnd.net
156570337 root-servers.net
165725087 amazonaws.com
175663948 akamai.net
185309527 weather.com
194943117 name-services.com
204902683 yahoo.com

## Slide 60
Name Resolution
Zone: collection of connected nodes with the same authoritative DNS server
Resolution method when answer not in cache:
Where is www.example.com?
Where is www.example.com?
Try com nameserver
Where is www.example.com?
Try example.com nameserver
Where is www.example.com?
208.77.188.166
208.77.188.166
Client
ISP DNS
Server
root
name server
com
name server
example.com
name server

## Slide 61: Iterative Name Resolution
Local Name Server
Application
Resolver
cache
google.com
Resolver
cache
.com
Resolver
cache
query
answer
answer
query
. (root)
Resolver
cache
1
2
3
query
answer

## Slide 62: DNS Caching
Step 1: query yourdomain.org
Local Machine
Application
Resolver
cache
Local NS
Resolver
cache
Authoritative
Name Server
Step 2: receive reply and cache at local NS and host
Local Machine
Application
Resolver
cache
Local NS
Resolver
cache
Authoritative
Name Server
query
query
answer
answer

## Slide 63: DNS Caching (con'd)
Step 3: use cached results rather than querying the ANS
Local Machine 1
Application
Resolver
cache
Local NS
Resolver
cache
Local Machine 2
Application
Resolver
cache
Step 4: Evict cache entries upon ttl expiration
query
answer