## Slide 1: Routing Security
Security, Privacy, and Consumer Protection Nick Feamster University of Chicago
Notes: Assignment 2: Wednesday
Midterm: October 24 (will cover material through this week)
Wednesday’s lecture: Recorded. Extra office hour TBD (Friday afternoon)

## Slide 2: Internet Routing Protocol: BGP
Route Advertisement
Autonomous Systems (ASes)
Session
Traffic
Destination Next-hop AS Path
128.135.0.0/16
128.135.0.0/16
192.5.89.89
66.250.252.44
10578..160
174… 160
Notes: Diagram of routing table is very confusing because it’s not pointing to anything
Green arrow shorter, and too thick… green is a msg
More intuition about how the system actually works.
Don’t say “interdomain”
DESTINATION-BASED Routing
Tables look like a set of possible routes and a rankings over these routes
(pop up a simplified table fragment)

## Slide 3: Border Gateway Protocol
Internet’s interdomain routing protocol, BGP, essentially has no security — will believe any routes advertised by neighboring router.
Different ways to interfere with Internet routing:
  Cut-off (Egypt case)
  BGP “route hijacking”

## Slide 5: China’s Accidental Hijack

## Slide 6: China Hijack: Sequence of Events
On April 8, 2010, China advertised about 50,000 blocks of IP addresses from 170 different countries
  60,000 prefixes from the US
Event lasted for 20 minutes
Why did most people not notice?
How might more traffic have been intercepted?
http://www.renesys.com/blog/2010/11/chinas-18-minute-mystery.shtml

## Slide 7
Notes: China Telecom’s AS 22724 hijacks Verizon Wireless’s prefix 66.174.161.0/24. The bogus route originated by AS 22724 propagates through the AS-level graph and is eventually selected by AT&T because it is shorter than the legitimate route originating at Verizon Wireless’s AS 22394. Meanwhile, Level3 selects the legitimate route, because it is shorter than the bogus route. Thus, network traffic splits between the hijacking AS and the legitimate origin AS, with the nature of the split depending on routing policies used by individual ASes and the topology of the AS-level graph.

## Slide 8: Other “Famous” Hijack Events
February 24, 2008: Pakistan advertises a small part of YouTube’s AS 36561
  Likely as a botched attempt to block YouTube in Pakistan, following a government order
January 22, 2006: Con Edison (AS 27605) mistakenly advertises lot of networks (Level 3, UUNet, Panix ISP, …)
April 25, 1995: AS 7007 incident
“Ultimately, though, the problem remains on of transitive trust. A provider can and should limit the advertisements it will accept from a customer.”

## Slide 9
Notes: Perhaps the most famous subprefix hijack occurred on February 24, 2008, when Pakistan Telecom took YouTube offline. The incident2 began when Pakistani authorities demanded that YouTube to be censored within Pakistan. To accomplish this, Pakistan Telecom’s AS 17557 launched a subprefix hijack by originating the subprefix 208.65.153.0/24 of YouTube’s prefix 208.65.153.0/22 to its customer ASes in Pakistan (e.g., Aga Khan University, Lahore Stock Exchange, Allied Bank Pakistan), as in figure 3.37,41 This meant that traffic destined for YouTube’s servers in AS 36561 would instead be forwarded to the longer IP prefix originated by Pakistan Telecom’s AS 17557, where traffic could then be dropped. Events took an unexpected turn when Pakistan Telecom’s bogus BGP announcement leaked out of Pakistan. PCCW, a large ISP that provides global network connectively to Pakistan Telecom, received the bogus routing announcement, selected the bogus route, and announced it to its own neighbors. Because the bogus route was for a longer prefix (/24) than the legitimate route (/22), longest-prefixmatch routing meant the bogus route was always more preferred by the legitimate route, and within minutes, at least two-thirds of the Internet was sending its YouTube traffic to Pakistan.2

## Slide 10: Attacks on Routing
How these attacks can happen
Compromised routers
Unscrupulous ISPs
Configuration error
Problems
Bogus origination of routes
Bogus modification of routes

## Slide 11: China’s Accidental Hijack

## Slide 12: China Hijack: Sequence of Events
On April 8, 2010, China advertised about 50,000 blocks of IP addresses from 170 different countries
  60,000 prefixes from the US
Event lasted for 20 minutes
Why did most people not notice?
How might more traffic have been intercepted?
http://www.renesys.com/blog/2010/11/chinas-18-minute-mystery.shtml

## Slide 13: Attacks against BGP
Tampering with routing software
Tampering with update data en route
Router compromise and “misconfiguration”
Tampering with router management software

## Slide 14: Intradomain Routing Security
Shared secrets guard against new machines being plugged in, but not against an authorized party being dishonest.
Solution: digitally sign each LSA (expensive!). List authorizations in certificate.
Note: everyone sees the whole map; monitoring station can note discrepancies from reality.

## Slide 15: Who Needs Origin Authentication?
Prefix hijacking
  Route leaks (cf. AS 7007 incident from L6)
  Redirection (e.g., for phishing)
  Blackholing traffic
  Spamming
De-aggregation attacks (or misconfiguration)
  Can be lethal when combined with hijacking

## Slide 16: Why Origin Auth Matters: Phishing
Hijacking DNS (cache poisoning)
Hijacking web server
In theory, SSL should protect, but…
Question: Why does path authentication matter?
BGP Route to authoritative DNS server
BGP Route to Web server

## Slide 17: Who Needs Origin Authentication?
Prefix hijacking
  Route leaks (cf. AS 7007 incident from L6)
  Redirection (e.g., for phishing)
  Blackholing traffic
  Spamming
De-aggregation attacks (or misconfiguration)
  Can be lethal when combined with hijacking

## Slide 18: Data Plane Security
No guarantees about the path that packets will actually traverse
S-BGP, soBGP do not protect against internal routing snafus
AS 1
AS 2
AS 3
AS Path = 1 2 …
Misconfiguration can cause packet deflections.

## Slide 19: What This Means
Rootkits + 0day  rogue announcements  Man-in-middle attacks, with our clues applied
  No need for three-way-handshake when you’re in-line
  Nearly invisible exploitation potential, globally
Endpoint enumeration - direct discovery of who and what your network talks to
Can be accomplished globally, any-to-any
How would you know if this isn’t happening right now to your traffic at DEFCON?

## Slide 20: BGP MITM Hijack Concept
We originate the route like we always did
  Win through usual means (prefix length, shorter as-path w/ several origin points, etc)
    “Win” is some definition of “most of the internet chooses your route”
We return the packets somehow
  Coordinating delivery was non-trivial
  Vpn/tunnel involve untenable coordination at target
Then it clicked – use the Internet itself as reply path, but how?

## Slide 21: BGP MITM Setup
Traceroute & plan reply path to target
Note the ASN’s seen towards target from traceroute & bgp table on your router
Apply as-path prepends naming each of the ASN’s intended for reply path
Nail up static routes towards the next-hop of the first AS in reply path
Done

## Slide 22: BGP MITM – First Observe
Random User ASN 100
Target ASN 200
AS20
AS10
AS30
AS60
AS40
AS50
ASN 200 originates 10.10.220.0/22, sends announcements to AS20 and AS30
Internet is converged towards valid route
View of Forwarding Information Base (FIB) for 10.10.220.0/22 after converging

## Slide 23: BGP MITM – Plan reply path
Attacker ASN 100
Target ASN 200
AS20
AS10
AS30
AS60
AS40
AS50
ASN 100’s FIB shows route for 10.10.200.0/22 via AS10
We then build our as-path prepend list to include AS 10, 20, and 200

## Slide 24: BGP MITM – Setup Routes
AS50
Attacker ASN 100
Target ASN 200
AS20
AS10
AS30
AS60
AS40
10.10.220.0/24 is announced with a route-map:
Then, install static route in AS100 for 10.10.220.0/24 to AS10’s link
ip route 10.10.220.0 255.255.255.0 4.3.2.1

## Slide 25: Anonymzing The Hijacker
We adjust TTL of packets in transit
Effectively ‘hides’ the IP devices handling the hijacked inbound traffic (ttl additive)
Also hides the ‘outbound’ networks towards the target (ttl additive)
Result: presence of the hijacker isn’t revealed

## Slide 26: Without TTL adjustment
2 12.87.94.9 [AS 7018] 4 msec 4 msec 8 msec
3 tbr1.cgcil.ip.att.net (12.122.99.38) [AS 7018] 4 msec 8 msec 4 msec
4 ggr2.cgcil.ip.att.net (12.123.6.29) [AS 7018] 8 msec 4 msec 8 msec
5 192.205.35.42 [AS 7018] 4 msec 8 msec 4 msec
6 cr2-loopback.chd.savvis.net (208.172.2.71) [AS 3561] 24 msec 16 msec 28 msec
7 cr2-pos-0-0-5-0.NewYork.savvis.net (204.70.192.110) [AS 3561] 28 msec 28 msec 28 msec
8 204.70.196.70 [AS 3561] 28 msec 32 msec 32 msec
9 208.175.194.10 [AS 3561] 28 msec 32 msec 32 msec
10 colo-69-31-40-107.pilosoft.com (69.31.40.107) [AS 26627] 32 msec 28 msec 28 msec
11 tge2-3-103.ar1.nyc3.us.nlayer.net (69.31.95.97) [AS 4436] 32 msec 32 msec 32 msec
12 * * * (missing from trace, 198.32.160.134 – exchange point)
13 tge1-2.fr4.ord.llnw.net (69.28.171.193) [AS 22822] 32 msec 32 msec 40 msec
14 ve6.fr3.ord.llnw.net (69.28.172.41) [AS 22822] 36 msec 32 msec 40 msec
15 tge1-3.fr4.sjc.llnw.net (69.28.171.66) [AS 22822] 84 msec 84 msec 84 msec
16 ve5.fr3.sjc.llnw.net (69.28.171.209) [AS 22822] 96 msec 96 msec 80 msec
17 tge1-1.fr4.lax.llnw.net (69.28.171.117) [AS 22822] 88 msec 92 msec 92 msec
18 tge2-4.fr3.las.llnw.net (69.28.172.85) [AS 22822] 96 msec 96 msec 100 msec
19 switch.ge3-1.fr3.las.llnw.net (208.111.176.2) [AS 22822] 84 msec 88 msec 88 msec
20 gig5-1.esw03.las.switchcommgroup.com (66.209.64.186) [AS 23005] 84 msec 88 msec 88 msec
21 66.209.64.85 [AS 23005] 88 msec 88 msec 88 msec
22 gig0-2.esw07.las.switchcommgroup.com (66.209.64.178) [AS 23005] 88 msec 88 msec 88 msec
23 acs-wireless.demarc.switchcommgroup.com (66.209.64.70) [AS 23005] 88 msec 84 msec 84 msec

## Slide 27: With TTL Adjustments
2 12.87.94.9 [AS 7018] 8 msec 8 msec 4 msec
3 tbr1.cgcil.ip.att.net (12.122.99.38) [AS 7018] 4 msec 8 msec 8 msec
4 ggr2.cgcil.ip.att.net (12.123.6.29) [AS 7018] 4 msec 8 msec 4 msec
5 192.205.35.42 [AS 7018] 8 msec 4 msec 8 msec
6 cr2-loopback.chd.savvis.net (208.172.2.71) [AS 3561] 16 msec 12 msec *
7 cr2-pos-0-0-5-0.NewYork.savvis.net (204.70.192.110) [AS 3561] 28 msec 32 msec 32 msec
8 204.70.196.70 [AS 3561] 28 msec 32 msec 32 msec
9 208.175.194.10 [AS 3561] 32 msec 32 msec 32 msec
10 gig5-1.esw03.las.switchcommgroup.com (66.209.64.186) [AS 23005] 88 msec 88 msec 84 msec
11 66.209.64.85 [AS 23005] 88 msec 88 msec 88 msec
12 gig0-2.esw07.las.switchcommgroup.com (66.209.64.178) [AS 23005] 84 msec 84 msec 88 msec
13 acs-wireless.demarc.switchcommgroup.com (66.209.64.70) [AS 23005] 88 msec 88 msec 88 msec

## Slide 28: Compare Original BGP & Route Path
Hijacked:
2 12.87.94.9 [AS 7018] 8 msec 8 msec 4 msec
3 tbr1.cgcil.ip.att.net (12.122.99.38) [AS 7018] 4 msec 8 msec 8 msec
4 ggr2.cgcil.ip.att.net (12.123.6.29) [AS 7018] 4 msec 8 msec 4 msec
5 192.205.35.42 [AS 7018] 8 msec 4 msec 8 msec
6 cr2-loopback.chd.savvis.net (208.172.2.71) [AS 3561] 16 msec 12 msec *
7 cr2-pos-0-0-5-0.NewYork.savvis.net (204.70.192.110) [AS 3561] 28 msec 32 msec 32 msec
8 204.70.196.70 [AS 3561] 28 msec 32 msec 32 msec
9 208.175.194.10 [AS 3561] 32 msec 32 msec 32 msec
10 gig5-1.esw03.las.switchcommgroup.com (66.209.64.186) [AS 23005] 88 msec 88 msec 84 msec
11 66.209.64.85 [AS 23005] 88 msec 88 msec 88 msec
12 gig0-2.esw07.las.switchcommgroup.com (66.209.64.178) [AS 23005] 84 msec 84 msec 88 msec
13 acs-wireless.demarc.switchcommgroup.com (66.209.64.70) [AS 23005] 88 msec 88 msec 88 msec
Original:
2 12.87.94.9 [AS 7018] 8 msec 8 msec 4 msec
3 tbr1.cgcil.ip.att.net (12.122.99.38) [AS 7018] 8 msec 8 msec 8 msec
4 12.122.99.17 [AS 7018] 8 msec 4 msec 8 msec
5 12.86.156.10 [AS 7018] 12 msec 8 msec 4 msec
6 tge1-3.fr4.sjc.llnw.net (69.28.171.66) [AS 22822] 68 msec 56 msec 68 msec
7 ve5.fr3.sjc.llnw.net (69.28.171.209) [AS 22822] 56 msec 68 msec 56 msec
8 tge1-1.fr4.lax.llnw.net (69.28.171.117) [AS 22822] 64 msec 64 msec 72 msec
9 tge2-4.fr3.las.llnw.net (69.28.172.85) [AS 22822] 68 msec 72 msec 72 msec
10 switch.ge3-1.fr3.las.llnw.net (208.111.176.2) [AS 22822] 60 msec 60 msec 60 msec
11 gig5-1.esw03.las.switchcommgroup.com (66.209.64.186) [AS 23005] 60 msec 60 msec 60 msec
12 66.209.64.85 [AS 23005] 64 msec 60 msec 60 msec
13 gig0-2.esw07.las.switchcommgroup.com (66.209.64.178) [AS 23005] 60 msec 64 msec 60 msec
14 acs-wireless.demarc.switchcommgroup.com (66.209.64.70) [AS 23005] 60 msec 60 msec 60 msec

## Slide 29: Control Plane Security: Authentication
Session Authentication/Integrity
  Who’s on the other end of that BGP session?
  Are the routing messages correct?
Path Authentication
  Is the AS path correct?
Origin Authentication
  Does the prefix of the route correspond to the AS that actually owns that prefix

## Slide 30: Session Authentication: TCP MD5
Authenticate packets received from a peer using TCP MD5.
Key distribution: manual.
Key rollover: vendor-dependent

## Slide 31: Session Authentication: TTL Hack
Insight: Most eBGP sessions are only a single hop; attackers typically are remote
Remote packet injection can’t have a TTL >= 254
eBGP
Transmits all
packets with a
TTL of 255
Doesn’t accept
packets with a TTL
lower than 254

## Slide 32: Proposals for Control Plane Security
S-BGP: Secure BGP
  PKI-based
  Signatures on every element of the path
soBGP: “Secure Origin” BGP
  Use PKI only for origin authentication
  Topology database for path authentication

## Slide 33: S-BGP
Address-based PKI: validate signatures
  Authentication of
    ownership for IP address blocks,
    AS number,
    an AS's identity, and
    a BGP router's identity
  Use existing infrastructure (Internet registries etc.)
  Routing origination is digitally signed
  BGP updates are digitally signed
Route attestations: A new, optional, BGP transitive path attribute
  carries digital signatures covering the routing information in updates

## Slide 34: Attestations: Update Format
Address attestation is usually omitted
Owning Org, NLRI, first Hop AS, SIG
Issuer, Cert ID, Validity, Subject, Path, NLRI, SIG
BGP Hdr: Withdrawn NLRI, Path Attributes, Dest. NLRI
Issuer, Cert ID, Validity, Subject, Path, NLRI, SIG
Issuer, Cert ID, Validity, Subject, Path, NLRI, SIG
Route Attestations
Address Attestation
Question: Why are there multiple route attestations?

## Slide 35: Attestation Format: More Details
Issuer: an AS
Certificate ID: for joining with certificate information received from third party
AS Path
Validity: how long is this routing update good?

## Slide 36: Reducing Message Overhead
Problem: How to distribute certificates, revocation lists, address attestations?
  Note: This data is quite redundant across updates
Solution: use servers for these data items
  replicate for redundancy & scalability
  locate at NAPs for direct (non-routed) access
  download options:
    whole certificate/AA/CRL databases
    queries for specific certificates/AAs/CRLs

## Slide 37: S-BGP Optimizations
Handling peak loads (e.g., BGP session reset)
  Extra CPUs
  Deferred verification
  Background verification of alternate routes
Observation: Most updates caused by “flapping”
  Cache previously validated routes

## Slide 38: Practical Problems with S-BGP
Requires Public-Key Infrastructure
Lots of digital signatures to calculate and verify.
  Message overhead
  CPU overhead
Calculation expense is greatest when topology is changing
  Caching can help
Route aggregation is problematic (maybe that’s OK)
Secure route withdrawals when link or node fails?
Address ownership data out of date
Deployment

## Slide 39: Public Key Infrastructure (PKI)
Problem: Key distribution
  How do you find out someone’s public key?
  How do you know it isn’t someone else’s key?
Root of PKI: Certificate Authority (CA)
  Bob takes public key and identifies himself to CA
  CA signs Bob’s public key with digital signature to create a certificate
  Alice can get Bob’s key (doesn’t matter how) and verify the certificate with the CA
PKIs are typically organized into hierarchies

## Slide 40: Address Block PKI is Natural

## Slide 41: Reducing Message Overhead
Problem: How to distribute certificates, revocation lists, address attestations?
  Note: This data is quite redundant across updates
Solution: use servers for these data items
  replicate for redundancy & scalability
  locate at NAPs for direct (non-routed) access
  download options:
    whole certificate/AA/CRL databases
    queries for specific certificates/AAs/CRLs

## Slide 42: Attack: Path Shortening Attack
AS Path = 2 4
AS 4
AS 1
AS 6
AS 2
AS 3
Adversary AS shortens AS path to divert traffic.

## Slide 43: Preventing Shortening in S-BGP
Why is this not possible in S-BGP?
AS Path = 2 4
AS 4
AS 1
AS 2
AS 3
Must be able to generate signature for AS Path “2 4”

## Slide 44: What Attacks Does S-BGP Not Prevent?
Message suppression: Failure to advertise route withdrawal
Replay attacks: Premature re-advertisement of withdrawn routes
Data plane security: Erroneous traffic forwarding, bogus traffic generation, etc. (not really a BGP issue)

## Slide 45: Secure Origin BGP (soBGP)
AS is authorized to originate a prefix
Advertised prefix is reachable within the origin AS
Peer that is advertising a prefix has at least one valid path to the destination
Three Goals

## Slide 46: Limitations of soBGP
BGP transport Connection
  Handled by MD5 authentication
Route attributes
The validity of the AS path
  Relies on consistency checks

## Slide 47: soBGP Design Constraints
No central authority
Incremental deployability
Deployment flexibility (on/off box cryptography, etc.)
Flexible signaling mechanism
Should not rely on routing to secure routing (No external database connection on system initialization).
Minimize impact to current BGPv4 implementations

## Slide 48: Step 1: AS Identity (EntityCert)
Each AS creates a public/private key pair (signed by third party)
The key and AS can be validated using the signer’s public key
PuK
Sig
AS
PuK
Sig
AS
PuK
Sig
AS
PuK
Sig
AS
PuK
Sig
AS
Signatures by trusted third party

## Slide 49: Step 2: Origin Authentication (AuthCert)
Sig
Sig
Signed certificate authorizes another AS to advertise a prefix
AS65501
10.1.0.0/16
AS65502
10.2.0.0/16
Sig
AS65503
10.1.1.0/24
Sig
AS65504
10.1.2.0/24
AS65500
10.0.0.0/8
AS65500
Public Key
Sig
AS65501
Public Key
Delegation
EntityCert
AuthCert

## Slide 50: Step 3: Policy Authentication (PolicyCert)
AS 65500
AS 65502
The longest prefix in 10.1.0.0/16 will be a /20.
AS65501
AS 65501
Each AS builds a certificate which contains policy information (e.g., maximum prefix length).

## Slide 51: Step 4: Path Authentication (PolicyCert)
Signed PolicyCert contains a signed list of peers PolicyCerts are flooded throughout the network
AS 1
AS 3
AS 2
AS 4
Question: How to prevent lying about false edges in PolcyCert?
I’m attached to AS 4

## Slide 52: Preventing Shortening in soBGP
If AS 3 attempts to make its path to AS 5 shorter by cutting AS 4 out of the path, AS 1 might be able to detect the alteration in the AS Path.
Problems:
  No protection against replay
  No protection, depending on topology
AS 1
AS 2
AS 3
AS 5
I’m attached to 1, 4, & 5
AS 4
I’m attached to 2 & 4
Now What? Must update PolicyCert?!

## Slide 53: Preventing False Edges in soBGP
AS 1
AS 2
AS 3
AS 4
AS 4 is behind me.
AS 4 is behind me.
I’m connected to AS 2
Two-way policy check will fail.
Possible denial-of-service attacks based on this mechanism?

## Slide 54: Preventing False Edges in S-BGP
AS 1
AS 2
AS 3
AS 4
AS 3 must be able to generate a signed route attestation for the path 3 4 (and whatever prefix that involves).
AS Path = 1 3 4

## Slide 55: Certificate Distribution in soBGP
Transport agnostic (distributed out of band)
  Possible problem: setting routes to distribute policy certs?
One mode of transport is provided in the soBGP drafts themselves:
  New BGP SECURITY message
Negotiated at session startup
  Certificates may be exchanged before routing
  Routing may be exchanged before certificates
  Certificates only may be exchanged

## Slide 56: Problems with soBGP
Integrity problems: Cannot validate that the update actually traversed the path (!)
Collusion: Colluding ASes can create false edges
PolicyCert/Topology map does not prevent against replay attacks (or advertising a path that has been recently withdrawn)
No security for withdrawals

## Slide 57: S-BGP vs. soBGP
Path authentication
Computational cost
Message overhead (bandwidth)
Memory
Administrative delay
  What is the process by which a new prefix can be added to the infrastructure
Accuracy of address ownership information
  Problem with both schemes

## Slide 58: S-BGP vs. soBGP: Requirements
 | soBGP | S-BGP
Does the AS Path exist? | Maybe: PolicyCerts | Yes
Did the received update travel along that path? | No | Yes: Route Attestation + Validity
Was the update authorized to traverse that path by the originator? | Maybe: Depends on how PolicyCerts are written | No