## Slide 1: Physical Security

## Slide 2
Let’s think like an attacker…

## Slide 6
(voting machine)

## Slide 7: What Is Physical Security?
Any physical object that creates a barrier to unauthorized access
This includes: locks, latches, safes, alarms, guards, guard dogs, doors, windows, walls, ceilings, floors, fences, door strikes, door frames and door closers

## Slide 8: Destructive vs. Nondestructive Entry
Destructive entry
  Involves using force to defeat physical security
  Methods involve crowbars, bolt cutters and sledge hammers
  Negative impact on IT resources is apparent
  Remediation steps also obvious
Nondestructive entry
  Compromises security without leaving signs of a breach
  Defeats intrusion detection
  Greater and long-term threat

## Slide 9: Is Physical Security An IT Concern?
You have been working hard to secure your network from cyber attacks
  Redundant layers of authentication, firewalls, and intrusion detection systems should protect against electronic methods of entry
But what if an attacker gains access to the server room or network wiring closet ...
  Is you network still safe?

## Slide 10: Type of Threats to Physical Environment
Natural / Environmental
  Earthquakes, floods, storms, hurricanes, fires, snow/ice
  Consequence of natural phenomena
Man made / Political Events
  Explosives, disgruntled employees, unauthorized access, employee errors, espionage, arson/fires, sabotage, hazardous/toxic spills, chemical contamination, malicious code, vandalism and theft
  Acts of commission or omission
© CISSP® Common Body of Knowledge Review

## Slide 11: Lessons-Learned for U.S.
Major Domestic Events:
  2005 Hurricane Katrina (1,836)
  2001 9/11 Attack: World Trade Center, Pentagon, and Shanksville, PA (2,982)
  1995 Federal Office Building, Oklahoma City (168)
Major International Events:
  1998 U.S. Embassy, Kenya (237)
  1983 Beirut Barracks, Lebanon (309)
© CISSP® Common Body of Knowledge Review

## Slide 12: Categories of Security Controls
Management (Administrative) Controls
  Policies, Standards, Processes, Procedures, & Guidelines
    Administrative Entities: Executive-Level, Mid.-Level Management
Physical Controls
  Physical Security (Facility or Infrastructure Protection)
    Locks, Doors, Walls, Fence, Curtain, etc.
    Service Providers: FSO, Security Guards, Dogs
Technical (Logical) Controls
  Access Controls , Identification & Authorization, Confidentiality, Integrity, Availability, Non-Repudiation.
    CCTV & Camera, IDS, Moisture detection system, Fire/Smoke detection system, Fire suppression, Environmental control system, UPS, etc.
    Service Providers: Building Architect, Critical Infrastructure Protection (CIP) Engineer, Operations Center.
© CISSP® Common Body of Knowledge Review

## Slide 13: Security Countermeasures & Technologies Strategic Approach to Physical Security …(2/2)
Defense-in-depth
Source: Global Crossing website

## Slide 14: Physical Controls – Facility Construction
Structured barriers: Perimeter structure
Walls & Fencing
  Specific gauge and fabrication specifications (e.g. No. 11 gauge galvanized chain-link fencing material.)
  Specify height, or need for “top guard” (e.g. 8-ft in height, 6-in. under ground with top guard.)
Height | Protection
1 meter / 3 – 4 ft | Deters casual trespassers
2 meter / 6 – 7 ft | Too high to climb easily
2.4 meter / 8 ft with top guard | Deters determined intruder
Source: Official (ISC)2 Guide to The CISSP Exam

## Slide 15: Physical Controls – Facility Construction
Structured barriers: Entry points
  Gates, bollards, roadways.
  Doors, windows, ventilation airways, manhole covers, etc.
  Department of State and DoD Anti-Ram Vehicle Barrier Certification Criteria (SD-STD-02.01):
Vehicle Weight: 15,000 lb. | 
Speed Rating | Speed at Impact
K4 | 30 mph
K8 | 40 mph
K12 | 50 mph
Reference: http://www.probarrier.com/faq/certify.asp
Vehicle Weight: 15,000 lb. | 
Penetration Rating | Penetration Distance
L3 | < 3 ft
L2 | 3 – 20 ft
L1 | 20 – 50 ft

## Slide 16: Technical Controls – Entrance Protection
Entry access control systems
Turnstiles
  Revolving doors that can be activated to “lock” and not allow unauthorized individuals to enter or leave facility
  To prevent “piggybacking”.
Mantraps
  Routing people through two stationary doorways
Fail-safe
  Door defaults to being unlocked.
Fail-secure
  Door defaults to being locked.

## Slide 17: Technical Controls
Entry access control systems – Locks
Mechanical locks:
  Key
  Combination locks
  Magnetic locks
Electronic locks:
  Combination lock
  Proximity / RFID badge
  Bio-metric

## Slide 18
How does one evade these controls?

## Slide 19: Social Engineering

## Slide 20: Scenario
You have conducted pen tests of your web site
You have a sophisticated ASA firewall sitting on the border which can use adaptive rule sets to detect potential attacks
You have security officers monitoring the inbound packet streams using SNORT to look for attacks
Your website is bulletproof…

## Slide 21: Scenario
But…and this really happened
At 3 am a guy walks up to the front lobby door and holds up a sign to the cleaning crew that says in English and Spanish “Perdi, mis llaves!”
The guy has an ID card that says “Marriott Elite Silver”. The crew lets him into the building.
Guy walks around and finds a locked door marked “Server Room”. Unfortunately, it’s a crypto lock.

## Slide 22: Scenario
Three guesses and no luck.
Guess what, the Armstrong ceiling tiles!
Turn over a trashcan, pop the tile, the wall the doesn’t go all the way up.
The guy climbs over the wall and is in the server room safe and sound.
Now, the guy walks over to your web server, pops Knoppix into the DVD drive and reboots the server.

## Slide 23: Scenario
With knoppix running, mount the hard drive, locate the windows passwords take a quick picture, reboot the server, remove the disk, exit the building.
The adminstrator password is “ScoobyDoo!”
Later that night, attempt to connect to the linux server which is available via ssh, login as root with password, well, you guessed it.
Dump all employee data with SS numbers, etc. from the database.

## Slide 24: The Social Engineering Threat
Spear Phishing, et. al
  This is the art of getting you to compromise your own systems
  “Click this link to reset your bank password”
True Social Engineering
  If I can talk my way past your guards, your security system, your fence, your locks, your guns and tasers, etc. You have already lost.
  Beware the human with the clipboard and laminated id card.

## Slide 25: Avoiding Social Engineering
Training, Training, Training
  Your individuals with access must be trained properly!
    EVERYONE must have their ID checked and be escorted
  Your staff must also be trained properly.
    Anyone without ID should be approached, politely.
    “Hi, may I help you find somone?”
  You must eliminate phishing attacks via regular and repeated training. You must test this on a regular basis.

## Slide 26: Locks and Keys

## Slide 27: Legal Notice
Laws regarding lock picking vary significantly state-by-state
In most states purchase and possession of dedicated lock picking tools is legal
  Penalties are raised significantly if you get caught using them in the commission of a crime
Public domain image from http://commons.wikimedia.org/wiki/File:Madame_Restell_in_jail.jpg

## Slide 28
http://toool.us/laws.html

## Slide 29: Lock Picking in Movies
Genuine lock picking in movies used to be prohibited
Before 1967, the Hays code (Motion Picture Production Code) required censorship of Hollywood movies
  “All detailed (that is, imitable) depiction of crime must be removed, such as lock picking or mixing of chemicals to make explosives”
Public domain image from http://commons.wikimedia.org/wiki/File:Motion_Picture_Production_Code.gif

## Slide 30: Pin Tumbler Lock

## Slide 35
Notes: Master Keyed Systems

## Slide 36: s
87 = 2,097,152

## Slide 37: Compromising Locks
For centuries, the lock has been one of the cornerstones of physical security
  We rely on dozens of them every day to protect people and assets
The trust most people place in locks is unwarranted
  Most locks can be easily compromised with nondestructive methods
  Sometimes within seconds and with readily available tools
“Locks keep honest people honest”

## Slide 38: Feeler Picking
Apply light tension
Lift one pin at a time
  Identify binding pin
Lift binding pin until it reaches the shear line
Setting the binding pin will rotate the lock slightly
Find next pin and repeat the process
Image from http://commons.wikimedia.org/wiki/File:Pin_and_tumbler_lock_picking.PNG used with permission under Gnu Free Documentation License 1.2

## Slide 39: Scrubbing / Raking
Apply light tension
Work over pins back to front in a circular motion
  attempting to pop them into the shear line with the combination of tension
Good for beginners
Usually employ snake pick or half diamond
Photo by Jennie Rogers included with permission.

## Slide 40: Bump Keys
Driver pins “jump” higher than the cylinder just for an instant
If a light rotational force is applied, the cylinder will turn
Lock bumping is a very fast method for opening the lock
The lock is not damaged
Defense: different weighted pins
Photo by Jennie Rogers included with permission.

## Slide 41
How many of you have your keys sitting out?

## Slide 45
Why is physical security an IT concern?

## Slide 46
physical access == total access?

## Slide 50
What about Encryption?

## Slide 51: Hibernation
Modern machines have the ability to go into a powered-off state known as hibernation.
While going into hibernation, the OS stores the contents of machine’s memory into a hibernation file (such as hiberfil.sys) on disk so the computer can be quickly restored later.
But… without additional security precautions, hibernation exposes a machine to potentially invasive forensic investigation.
1. User closes a laptop computer,
putting it into hibernation.
2. Attacker copies the hiberfil.sys
file to discover any unencrypted
passwords that were stored
in memory when the computer
was put into hibernation.

## Slide 53
Proximity

## Slide 54: Signal Emissions
Computer screens emit radio frequencies that can be used to detect what is being displayed.
Visible light reflections can also be used to reconstruct a display from its reflection on a wall, coffee mug, or eyeglasses.
Both of these require the attacker to have a receiver close enough to detect the signal.

## Slide 56: Faraday Cages
To block electromagnetic emanations in the air, we can surround sensitive equipment with metallic conductive shielding or a mesh of such material, where the holes in the mesh are smaller than the wavelengths of the electromagnetic radiation we wish to block.
Such an enclosure is known as a Faraday cage.

## Slide 57: Acoustic Emissions
Dmitri Asonov and Rakesh Agrawal published a paper in 2004 detailing how an attacker could use an audio recording of a user typing on a keyboard to reconstruct what was typed.