## Slide 1: Lecture 11 – Networking Concepts
Michael Bailey
University of Illinois
ECE 422/CS 461 – Fall 2015

## Slide 2: Who recognizes this?
int sockfd;
struct sockaddr_in addr;
addr.sin_family = AF_INET;
addr.sin_addr.s_addr =
inet_addr(SERV_HOST_ADDR);
addr.sin_port = htons(SERV_TCP_PORT);
sockfd = socket(AF_INET, SOCK_STREAM, 0);
connect(sockfd, (struct sockaddr *) &addr,
sizeof(serv_addr));
do_stuff(stdin, sockfd);

## Slide 3: Classic view of network API
Start with host name (maybe)
foo.bar.com

## Slide 4: Classic view of network API
Start with host name
Get an IP address
foo.bar.com
gethostbyname()
10.5.4.3

## Slide 5: Classic view of network API
Start with host name
Get an IP address
Make a socket (protocol, address)
foo.bar.com
gethostbyname()
10.5.4.3
sock_id
socket();connect();…

## Slide 6: Classic view of network API
Start with host name
Get an IP address
Make a socket (protocol, address)
Send byte stream (TCP) or packets (UDP)
foo.bar.com
gethostbyname()
10.5.4.3
sock_id
socket();connect();…
TCP sock
UDP sock
Network
1,2,3,4,5,6,7,8,9 . . .
…
Eventually arrive in order
May or may not arrive

## Slide 7: Circuit and Packet Switching
Circuit switching
  Legacy phone network
  Single route through sequence of hardware devices established when two nodes start communication
  Data sent along route
  Route maintained until communication ends
Packet switching
  Internet
  Data split into packets
  Packets transported independently through network
  Each packet handled on a best efforts basis
  Packets may follow different routes

## Slide 8: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 9: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 10: Packet Switching
A
C
B
D
F
D
3
2
1

## Slide 11: Packet Switching
A
C
B
D
F
D
2
3
1

## Slide 12: Network Layers
Network models typically use a stack of layers
  Higher layers use the services of lower layers via encapsulation
  A layer can be implemented in hardware or software
  The bottom-most layer must be in hardware
A network device may implement several layers
A communication channel between two nodes is established for each layer
  Actual channel at the bottom layer
  Virtual channel at higher layers

## Slide 13: Internet Layers
Application
Transport
Network
Link
Application
Transport
Network
Link
Network
Link
Network
Link
Ethernet
Fiber Optics
Wi-Fi
Physical Layer

## Slide 14: Protocols
A protocol defines the rules for communication between computers
Protocols are broadly classified as connectionless and connection oriented
Connectionless protocol
  Sends data out as soon as there is enough data to be transmitted
  E.g., user datagram protocol (UDP)
Connection-oriented protocol
  Provides a reliable connection stream between two nodes
  Consists of set up, transmission, and tear down phases
  Creates virtual circuit-switched network
  E.g., transmission control protocol (TCP)

## Slide 15: Encapsulation
A packet typically consists of
  Control information for addressing the packet: header and footer
  Data: payload
A network protocol N1 can use the services of another network protocol N2
  A packet p1 of N1 is encapsulated into a packet p2 of N2
  The payload of p2 is p1
  The control information of p2 is derived from that of p1
Header
Payload
Footer
Header
Payload
Footer

## Slide 16: Internet Packet Encapsulation
Application Packet
TCP Data
TCP
Header
IP
Header
Frame
Header
Frame
Footer
Link Layer
Network Layer
Transport Layer
IP Data
Frame Data
Application Layer

## Slide 17: Network Interfaces
Network interface: device connecting a computer to a network
  Ethernet card
  WiFi adapter
A computer may have multiple network interfaces
Packets transmitted between network interfaces
Most local area networks, (including Ethernet and WiFi) broadcast frames
In regular mode, each network interface gets the frames intended for it
Traffic sniffing can be accomplished by configuring the network interface to read all frames (promiscuous mode)

## Slide 18: MAC Addresses
Most network interfaces come with a predefined MAC address
A MAC address is a 48-bit number usually represented in hex
  E.g., 00-1A-92-D4-BF-86
The first three octets of any MAC address are IEEE-assigned Organizationally Unique Identifiers
  E.g., Cisco 00-1A-A1, D-Link 00-1B-11, ASUSTek 00-1A-92
The next three can be assigned by organizations as they please, with uniqueness being the only constraint
Organizations can utilize MAC addresses to identify computers on their network
MAC address can be reconfigured by network interface driver software
Notes: MAC addresses can be permanently burned in (BIA), or be a locally administered address (LAA) set by an administrator. A MAC address starting out with 00-08-74 for instance is assigned by Dell, while one starting out with 00-0a-95 is assigned by Apple. Despite the IEEE limitations on LAAs, most OSs allow you to specify an arbitrary MAC for an interface.

## Slide 19: Switch
A switch is a common network device
  Operates at the link layer
  Has multiple ports, each connected to a computer
Operation of a switch
  Learn the MAC address of each computer connected to it
  Forward frames only to the destination computer

## Slide 20: Combining Switches
Switches can be arranged into a tree
Each port learns the MAC addresses of the machines in the segment (subtree) connected to it
Fragments to unknown MAC addresses are broadcast
Frames to MAC addresses in the same segment as the sender are ignored

## Slide 21: Types of Wireless Networks
Infrastructure
  Client machines establish a radio connection to a special network device, called access point
  Access points connected to a wired network, which provides a gateway to the internet
  Most common type of wireless network
Peer-to-peer
  Multiple peer machines connect to each other
  Typically used in ad-hoc networks and internet connection sharing
Access Point
Client
Wired LAN
Client
Client
Peer
Peer
Peer
Peer

## Slide 22: Internet Protocol
Connectionless
  Each packet is transported independently from other packets
Unreliable
  Delivery on a best effort basis
  No acknowledgments
  Packets may be lost, reordered, corrupted, or duplicated
IP packets
  Encapsulate TCP and UDP packets
  Encapsulated into link-layer frames
Data link frame
IP packet
TCP or UDP packet

## Slide 23: IP packet layout
IP header includes
  Source address
  Destination address
  Packet length (up to 64KB)
  Time to live (up to 255)
  IP protocol version
  Fragmentation information
  Transport layer protocol information (e.g., TCP)

## Slide 24: IPv4 Packet Header Format
4-bit
version
4-bit
hdr len (bytes)
8-bit
Type of Service
(TOS)
16-bit total length (bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit header checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload (e.g., TCP/UDP packet, max size?)
20-byte
Header
usually IPv4
usually 20 bytes (without options)
IP fragmentation
error
check
header
max number
remaining hops
(decremented at
each router)
upper layer protocol
to deliver payload to,
e.g., ICMP (1), UDP (17), TCP (6)
e.g. timestamp,
record route
taken, specify
route

## Slide 25: IP Addressing
IP address used to route datagrams through network.
IPv4 32 bit address, IPv6 128 bit address.
Divided into two parts: network and host.
Network part: Used to route packets. (ZIP code)
Host part: Used to identify an individual host. (House number)
Usually represented in dotted decimal notation: 141.211.144.212
Each number represents 8 bits: 0-255.

## Slide 26: Decimal representation of Internet addresses
octet 1
octet 2
octet 3
Class A:
1 to 127
0 to 255
0 to 255
1 to 254
Class B:
128 to 191
Class C:
192 to 223
224 to 239
Class D (multicast):
Network ID
Network ID
Network ID
Host ID
Host ID
Host ID
Multicast address
0 to 255
0 to 255
1 to 254
0 to 255
0 to 255
0 to 255
0 to 255
0 to 255
0 to 255
Multicast address
0 to 255
0 to 255
1 to 254
240 to 255
Class E (reserved):
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
240.0.0.0 to
255.255.255.255
Range of addresses

## Slide 27: Classless Interdomain Routing (CIDR)
Allow division between network and host portion on any bit boundary.
  More efficient use of address space.
  Allows division/aggregation of sub-assignments.
Networks now identified by network address and the length of the network portion: 141.213.8.0/24
Hosts identified by address and network mask: 141.213.8.1, 255.255.255.0.
WHY? Rapid depletion of class B address space and poor utilization of the assigned address space

## Slide 28: IP subnets
CIDR prefix length | Subnet Mask | Number of hosts
/8 | 255.0.0.0 | 224
/9 | 255.128.0.0 | 223
/10 | 255.192.0.0 | 222
/24 | 255.255.255.0 | 28 = 256
/25 | 255.255.255.128 | 27 = 128
/26 | 255.255.255.192 | 26 = 64
/27 | 255.255.255.224 | 25 = 32
/28 | 255.255.255.240 | 24 = 16
/29 | 255.255.255.248 | 23 = 8
/30 | 255.255.255.252 | 22 = 4

## Slide 29: Transmission Control Protocol
TCP is a transport layer protocol guaranteeing reliable data transfer, in-order delivery of messages and the ability to distinguish data for multiple concurrent applications on the same host
Most popular application protocols, including WWW, FTP and SSH are built on top of TCP
TCP takes a stream of 8-bit byte data, packages it into appropriately sized segment and calls on IP to transmit these packets
Delivery order is maintained by marking each packet with a sequence number
Every time TCP receives a packet, it sends out an ACK to indicate successful receipt of the packet.
TCP generally checks data transmitted by comparing a checksum of the data with a checksum encoded in the packet

## Slide 30: Ports
TCP supports multiple concurrent applications on the same server
Accomplishes this by having ports, 16 bit numbers identifying where data is directed
The TCP header includes space for both a source and a destination port, thus allowing TCP to route all data
In most cases, both TCP and UDP use the same port numbers for the same applications
Ports 0 through 1023 are reserved for use by known protocols.
Ports 1024 through 49151 are known as user ports, and should be used by most user programs for listening to connections and the like
Ports 49152 through 65535 are private ports used for dynamic allocation by socket libraries

## Slide 31: TCP Packet Format
Bit Offset | 0-3 | 4-7 |  | 8-15 | 16-18 | 19-31
0 | Source Port |  |  |  | Destination Port | 
32 | Sequence Number |  |  |  |  | 
64 | Acknowledgment Number |  |  |  |  | 
96 | Offset | Reserved | Flags |  | Window Size | 
128 | Checksum |  |  |  | Urgent Pointer | 
160 | Options |  |  |  |  | 
>= 160 | Payload |  |  |  |  | 

## Slide 32: Establishing TCP Connections
TCP connections are established through a three way handshake.
The server generally has a passive listener, waiting for a connection request
The client requests a connection by sending out a SYN packet
The server responds by sending a SYN/ACK packet, indicating an acknowledgment for the connection
The client responds by sending an ACK to the server thus establishing connection
SYN
Seq = x
SYN-ACK
Seq = y
Ack = x + 1
ACK
Seq = x + 1
Ack = y + 1

## Slide 33: TCP Data Transfer
During connection initialization using the three way handshake, initial sequence numbers are exchanged
The TCP header includes a 16 bit checksum of the data and parts of the header, including the source and destination
Acknowledgment or lack thereof is used by TCP to keep track of network congestion and control flow and such
TCP connections are cleanly terminated with a 4-way handshake
  The client which wishes to terminate the connection sends a FIN message to the other client
  The other client responds by sending an ACK
  The other client sends a FIN
  The original client now sends an ACK, and the connection is terminated
Notes: Sequence numbers are 32 bit numbers, wrapping to 0. ACKs include sequence number for the received package so sender can keep track of packets received by the receiver.

## Slide 34: TCP Data Transfer and Teardown
Data seq=x
Ack seq=x+1
Data seq=y
Ack seq=y+1
Client
Server
Client
Server
Fin seq=x
Ack seq=x+1
Fin seq=y
Ack seq=y+1

## Slide 35: Autonomous Systems (AS)
The Internet is a collection of autonomous systems.
AS: A set of routers and networks under the same administrative control.
Inter-domain vs. intra-domain routing.
R1
R5
R4
R2
R6
R3

## Slide 36: IP Routing
A router bridges two or more networks
  Operates at the network layer
  Maintains tables to forward packets to the appropriate network
  Forwarding decisions based solely on the destination address
Routing table
  Maps ranges of addresses to LANs or other gateway routers

## Slide 37: Interplay between routing and forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 38: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
BGP provides each AS a means to:
  Obtain subnet reachability information from neighboring ASs.
  Propagate the reachability information to all routers internal to the AS.
  Determine “good” routes to subnets based on reachability information and policy.
Allows a subnet to advertise its existence to rest of the Internet: “I am here”

## Slide 39: BGP basics
Pairs of routers (BGP peers) exchange routing info over semi-permanent TCP connections: BGP sessions
Note that BGP sessions do not correspond to physical links.
When AS2 advertises a prefix to AS1, AS2 is promising it will forward any datagrams destined to that prefix towards the prefix.
  AS2 can aggregate prefixes in its advertisement
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
eBGP session
iBGP session

## Slide 40: DNS: Domain Name System
People: many identifiers:
  SSN, name, passport #
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., www.eecs.umich.edu - used by humans
Q: map between IP addresses and name ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol host, routers, name servers to communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 41: DNS name servers
no server has all name-to-IP address mappings
local name servers:
  each ISP, company has local (default) name server
  host DNS query first goes to local name server
authoritative name server:
  for a host: stores that host’s IP address, name
  can perform name/address translation for that host’s name
Why not centralize DNS?
single point of failure
traffic volume
distant centralized database
Maintenance
doesn’t scale!

## Slide 42: Name Space Distribution
124537172 arin.net
217003127 verisign.com
314529802 apnic.net
414526895 gslb.com
510917319 manitu.net
69167881 sorbs.net
78701029 msft.net
88595104 google.com
97520954 amazon.com
107450839 register.com
117034622 gtld-servers.net
126937887 facebook.com
136779616 coremetrics.com
146574735 msecnd.net
156570337 root-servers.net
165725087 amazonaws.com
175663948 akamai.net
185309527 weather.com
194943117 name-services.com
204902683 yahoo.com

## Slide 43: Iterative Name Resolution
Local Name Server
Application
Resolver
cache
google.com
Resolver
cache
.com
Resolver
cache
query
answer
answer
query
. (root)
Resolver
cache
1
2
3
query
answer

## Slide 44: DNS Caching
Step 1: query yourdomain.org
Local Machine
Application
Resolver
cache
Local NS
Resolver
cache
Authoritative
Name Server
Step 2: receive reply and cache at local NS and host
Local Machine
Application
Resolver
cache
Local NS
Resolver
cache
Authoritative
Name Server
query
query
answer
answer

## Slide 45: DNS Caching (con'd)
Step 3: use cached results rather than querying the ANS
Local Machine 1
Application
Resolver
cache
Local NS
Resolver
cache
Local Machine 2
Application
Resolver
cache
Step 4: Evict cache entries upon ttl expiration
query
answer